Spike Frequency Adaptation
- Model Sensory Adaptation in Neuromorphic Hardware
  - Model Sensory Adaptation using adaptive integrate and fire neurons
    - Model the circuit
      - Model the submechanism of the circuit
        - Model STD
        - Model STF
        - Model SFA in a manner that let's us build a sensory adaptation network
          - Model SFA in a manner that is biologically similar to the neurons we think are present in the cortical circuit
            - PC
            - SST
            - PV
            - GN

---
I={I_thap} over {I_{%tau ahp}} I_{Ca average}(1-e^{-t/%tau})

---
General SFA Metrics
F_adap= {F_init-F_ss} over {F_init }
Layer	2 to 4	5 to 6
T_adap	3-24 ms	50 ms
F_adap	55-80%	35-65%
F_adap and T_adap correleate significantly with cortical depth

---
END OF SFA Section
Therefore, Adaptation at a time scale exceeding the 100s of milliseconds is not attributed to single neuron behavior

---
Signal Chain of Perception
Stage 1: Will we see long term effect of adaptation in this three neuron circuit?
Layer 4 S1
PC
PV
SST
Third order neuron
First order
neuron
mechanoreceptors
Second order
neuron
Layer 6 S1
VPM & VPL
In the thalamus
Gracili & Cuneatus Nuclei in M.O.
Dorsal root Ganglion
Stage 4
Cortex
Stage 1
Stage 2
Stage 3

---
Question
- Will the double inhibition mechanism of layer 4 have any effect in the long time constant scale of 400’s as described in the giacomo valle paper?
  - The only way to answer it is to try and model it. Or in vivo experiments, but Im not in that department
Layer 4 S1
Third order neuron
Layer 4 S1 circuits: What do they know? Do they know things? Lets find out!!!
Stage 1

---
Cell Types in the Somatosensory cortex
- Exitatory L4
  - Stellate
  - Star Pyramid
  - Pyramidal Cells
Regular Spiking, local connections within L4
Kim, Taehyeon, Bryan M. Hooks, and Claire EJ Cheetham. "Circuit development in somatosensory cortex." Neural Circuit and Cognitive Development. Academic Press, 2020. 143-166.
Connections from L4 Stelate
Then out to L2/3
Regular Spiking

---
Cell Types in the Somatosensory cortex
- Inhibitory
  - PV+
    - Basket
    - Chandelier
  - SST+
    - Martinotti
    - Non-matinotti
  - 5HT3aR
    - VIP
    - Single Basket
    - Neurogliaform cells
Fast Spiking
Low threshold spiking?
Not in the model for now
Kim, Taehyeon, Bryan M. Hooks, and Claire EJ Cheetham. "Circuit development in somatosensory cortex." Neural Circuit and Cognitive Development. Academic Press, 2020. 143-166.

---
PC(Regular Firing)
Property	Value	SD	Sources
Membrane time constant ms	25.3	19.08	NeuroElectro
Spontaneous Firing rate Hz	1.5	.94	Neuro Electro
SS at Threshold Hz	12.3*	5.5	Beierlein 6 Gibson 2003
Maximal steady-state firing Rate Hz	59.4	13.7	Beierlein & Gibson 2003
- Types
  - Pyramidal
  - Stellate
  - Pyramidal Start
- In literature they all seem interchangable, but Stellate receive the inputs
- I tau = 2.8pA

---
PV(Fast Firing)
Property	Value	SD	Sources
Membrane time constant	9.57	4	NeuroElectro
Spontaneous Firing rate	5.32	3.98	NeuroElectro
SS at Threshold	56.5*	18.6	Beierlein 6 Gibson 2003
Maximal steady-state firing Rate Hz	271.1*(80**)	51.8	Beierlein & Gibson 2003
- Info
  - Basket or Chandelier Cells, I believe both behave the same, the projection location is the main difference
  - Fast Firing (Both Chandelier and Basket are fast firing)
- Tuning Parameters
  - I_tau= 7.5 pA
  - Alpha<1 for positive second derivative

---
SST(Martinotti Cells)(LTS)
Property	Value	SD	Sources
Membrane time constant	19.88	9.07	NeuroElectro
Spontaneous Firing rate
SS at Threshold	17.2*	7.9	Beierlein 6 Gibson 2003
Maximal steady-state firing Rate Hz	120.7	41.2	Beierlein & Gibson 2003
- LTF??
- Alpha<1 for positive second derivative
- I_tau=3.5
- PFB could be further tuned
- Should only be activated at high frequencies and inhibit PC more closelt

---
Guidelines to Simulation
- PV>PC>SST in terms of time constants and firing rate
- 1/10 gain from stimulus
- CV(ISI)² < 1 but as close to one as possible
  - Except when the stimulus is on, it can be closer to 0
- PV cells should not exhibit adaptation
- Maximum firing rate of 200hz for all neurons
- SST no spontanous firing rate, PC and PV around 10* (in biology is 1 or 5)
- SST shhould be LTS (but this is tricky and counter intuitive, cause its suppose to fire less than the other two)

---
Depression with the old equation but corrected
- With update rule on the old code
  - dD/dt=M(1-D)
- On Pre:
  - D = (D*(1-d))*(D<1) + 1*(D>=1)
  - Iampa += ((D*(D<1) + 1*(D>=1)))*Iampa_w0*weight

---
Network Simulations
P=0.9 AMPA
PC
(RS)
P=1 AMPA STD
P=0.9 AMPA
P=0.9 AMPA STD
P=1 AMPA STD
P=0.9 GABA_B
P=0.9 GABA_B
PV
(FS)
P=0.9 GABA_B
SST
(LTS)
P=1 AMPA STD
P=0.9 GABA_B
P=0.9 GABA_B
P=0.9 GABA_B
Third order neuron

---
Setting up the simulation from ground up
First, PC neuron Characteristics
Output firing rate 1 = [13.] Hz Output firing rate 2 = [23.] Hz Output firing rate 3 = [35.] Hz Output firing rate 4 = [50.] Hz
Membrane Time Constant= [25.32928065]
Adaptation Time Constant= [47.28132388]
Adaptation of
46.10837438423642
45.901639344262456
34.618755477651206
14.325842696629282
- adaptation_conf = {
- "Isoma_dpi_tau" : 2.8* pA,
- "Isoma_th" : 30 * nA,
- "alpha_soma": 4,
- "Isoma_ahp_tau": 3 * pA,
- "Isoma_ahp_w" : 70 * pA,
- "alpha_ahp" : 15,
- "soma_refP": 2 * ms,
- "Isoma_const": 150 *pA
- }
- ampa_conf = {"Iampa_tau": 5 * pA,
- "alpha_ampa": 4,
- "Iampa_w0": 20 * pA}
Long Time Constant
High adaptation ratio (Upward of 40% to 60%)
Fast adaptation (20-60ms)
Low gain 100 to 13hz 1000 to 50hz

---
Step 1, just PC
20 hz
No irregularity
No recurrency
Average firing rate in populations PC:3.6 PV: 0 SST: 0
Maximum firing rate in populations PC:4. Hz PV: 0 SST: 0
Cv Squared Values are PC:0.016687296099239787 PV: 100 SST: 100

---
Added Recurrency, burstiness ensued connec prob=.3
w=15
w=10

---
 Step 2 Tuned Irregularity
freq 20 and weight 8
No Input No recurrency
SST did not fire in the whole simulation SST has no spikes Average firing rate in populations
PC:2.4 PV: 11.0 SST: 0
Maximum firing rate in populations
PC:5. Hz PV: 11. Hz SST: 0
Cv Squared Values are
PC:0.018805953777693032 PV: 0.3240960228557467 SST: 100
The values are really regular but maybe its ok?, if anything, atleast PV is firing more than PC spontanously

---
 Step 3 EI connected
Input_ 100hz for 1 sec 5 weight PC PV
PVPC and PCPV weight, start at 10 then sweep
CV squared values where ok but we can do better
SST did not fire in the whole simulation
SST has no spikes
Average firing rate in populations PC:5.63 PV: 7.0 SST: 0
Maximum firing rate in populations PC:7.5 Hz PV: 7. Hz SST: 0
Cv Squared Values are PC:0.45285838147728574 PV: 0.428884904394091 SST: 100

---
Parameter sweep
At first we got nothing sad
Increased connection probabilities to .6 from .4 and .3 in between PVPC and PCPV
And PC PC to 20
Moved Number of neurons to 40 baseline
Input weight from 5 to

---
PV Cells now
First, PC neuron Characteristics
Output firing rate 1 = [13.] Hz Output firing rate 2 = [23.] Hz Output firing rate 3 = [35.] Hz Output firing rate 4 = [50.] Hz
Membrane Time Constant= [25.32928065]
Adaptation Time Constant= [47.28132388]
Adaptation of
46.10837438423642
45.901639344262456
34.618755477651206
14.325842696629282
- adaptation_conf = {
- "Isoma_dpi_tau" : 2.8* pA,
- "Isoma_th" : 30 * nA,
- "alpha_soma": 4,
- "Isoma_ahp_tau": 3 * pA,
- "Isoma_ahp_w" : 70 * pA,
- "alpha_ahp" : 15,
- "soma_refP": 2 * ms,
- "Isoma_const": 150 *pA
- }
- ampa_conf = {"Iampa_tau": 5 * pA,
- "alpha_ampa": 4,
- "Iampa_w0": 20 * pA}
Adaptation should not occurr